DFG-CNRS evaporating bubble experiment

Fluid:  	n-butane at initially nearly boiling condition, pressure about 2.8 bar at laboratory temperature of 17 degrees Celsius

Time between frames : 31ms

Exposure time: 1ms

Pressure drop: 0.360 bar/sec

Pressure drop: 0.006 bar/frame (average)

Data files:

1.	2xImager-90deg-scale-bothlights-nopressdrop

no pressure drop (only seeding), double imaging from orthogonal viewpoints

(0 mm corresponds to 95mm above bubble source), movie frames 95-191

Comment:	bubbles stay very small, observed meandering while moving upward.

It was decided to apply a pressure drop for following experiments to introduce enforced boiling

2.1	2xImager-90deg-scale-bothlights-pressdrop3

with pressure drop, double imaging from orthogonal viewpoints,

(0 mm corresponds to 95mm above bubble source), movie frames 200-280

2.2	2xImager-90deg-scale-bothlights-pressdrop4

with pressure drop, double imaging from orthogonal viewpoints,

(0 mm corresponds to 95mm above bubble source), movie frames 60-130

2.3	2xImager-90deg-scale-bothlights-pressdrop6

with pressure drop, double imaging from orthogonal viewpoints

(0 mm corresponds to 95mm above bubble source), movie frames 52-140

3.1	28mm-imaging-only-nopressdrop

Single shot, no pressure drop, full height view, movie frames 30-100

3.2.1	28mm-imaging-only-pressdrop2

Single shot, with pressure drop, full height view, movie frames 31-120

3.2.2 	28mm-imaging-only-pressdrop13

Single shot, with pressure drop, full height view, movie frames 40-120

4.1     35mm-imaging-only-pressdrop1

single shot, with pressure drop (0 mm corresponds to 95mm above bubble source), movie frames 55-120

4.2     35mm-imaging-only-pressdrop8

single shot, with pressure drop (0 mm corresponds to 95mm above bubble source), movie frames 50-140